Blowing up a polytropic star
Justin Lietz – Code
Kaitlin Cook – Analysis
Sherwood Richers – Inputs

---
Motivations
- Toy model of a star + toy model of a shock = toy supernova.
- We can then follow the nucleosynthesis.
- Acts as a good way to combine the tools from last week

---
Aims
Lane Emden
star
Sedov blast
Lagrangian VH1
Dimensionalise
XNET

---
Key Challenges
- Working out the realistic units
- Recasting VH1 in Lagrangian coordinates
- Writing a wrapper script to take output from VH1 to XNET
- Displaying the results in a meaningful way.

---
Polytropic Stars: Lane-Emden Solutions
Plot of a solution to Lane-Emden n = 5/3
Poisson Equation:
Hydrostatic Equilibrium:
Polytropic EOS:
Lane-Emden:

---
Sedov Blasts
- The Sedov blast - a large amount of energy in a small region.
- Simulate this by having a very high pressure in the first zone, smaller pressures in all of the other zones (from star model)

---
Lagrangian Coordinates
- Want to follow the nucleosynthesis of packet of stellar matter.
- Eulerian coordinates – matter passes between the zone boundaries.
- Lagrangian coordinates – moves the zone boundaries so each zone follows the matter packet.

---
VH1 Lagrangian
- VH1 computes the hydrodynamic flow using Lagrangian coordinates on each step, then remaps the information back onto an Eulerian grid.
- We got rid of the Eulerian remap from the ppmlr.f90 file so that the code remains in Lagrangian coordinates.

---
Lagrangian vs Eulerian

---
Connecting VH1 to Xnet
VH1 output looks familiar to a lot of you by now:

---
Hydro Results – 1Msol + 1041 ergs

---
10 Msol + 1041 ergs

---
1 Msol Blast at different radii

---
Nucleosynthesis 1 Msol + 1041 ergs zone 30

---
Nucleosynthesis 1 Msol + 1041 ergs zone 150

---
Nucleosynthesis 1 Msol + 1041 ergs zone 300

---
50/50 n/p progenitor

---
4He progenitor

---
58Fe progenitor

---
Abundances at t = 105
n+p initial
4He initial
56Fe initial

---
With a few more days?
- Add in gravity
- Different EOS
- More realistic initial conditions for hydro
- Further variation of initial abundances
- Vary blast energy
- Nucleosynthesis on all zones